## Slide 1
Multi-Angle Implementation of Atmospheric Correction (MAIAC)
Alexei Lyapustin, GSFC, code 613
Y. Wang (UMBC), S. Korkin (USRA)
NASA Direct Readout Webinar
May 29, 2018

## Slide 2
MAIAC: General Information
Status:
  C6 MODAPS re-processing of MODIS is finished (MCD19)
  MAIAC is on NASA Near Real Time Processing System
  Products (gridded):
  Atmosphere (MCDA2 - daily): CWV, CM, AOD, aerosol type (background/smoke/dust), Smoke Plume Height @1km resolution;
  Land Surface (A1 – daily; A3 – 8-day):
    - (MCDA1): spectral BRF (surface reflectance) @1km (B1-B13) and 500m (B1-B7); SigBRFn_B1,B2. Will add 250m in C6.1;
    - (MCDA3 – 8-day): BRDF (RTLS model, naturally gap-filled), instantaneous albedo (B1-B8); Will drop B8 from C6.1, instead provide B3-scaling factor;
  Detected Snow (A1): snow grain size, and sub-pixel snow fraction (1km);

## Slide 3
Multi-Angle Implementation of Atmospheric Correction (MAIAC)
Grid TOA L1B data to 1km fixed grid – work with polar-orbit data as “geostationary-like”;
Sliding window algorithm – store 4-16 last days of measurements in memory;
RT with fully coupled BRDF model;
Accumulate surface-related information for each grid cell (spectral BRDF, BT-contrasts etc.)
Features
Main Results
Advanced cloud (snow) detection – particular improvements over tropics and at northern lat. (vegetation analysis);
AOD data globally over dark and bright land surface;
Aerosol at 1km resolution & low urban bias – strong interest from AQ community;

## Slide 4
MODIS, TOA RGB
NBRF
AOT
BRF
MAIAC = Time Series + Spatial Analysis

## Slide 5
MAIAC Aerosol Type (Smoke/Dust)
Lyapustin, A. et al., 2012: Discrimination of biomass burning smoke and clouds in MAIAC algorithm, ACP, 12, 9679–9686.
Phys. principles (~OMI) – enhanced shortwave
absorption (Red Blue DB)
ni increases RDB for OC (smoke) and dust;
Multiple scattering, for absorbing aerosols.
Backgr./Smoke/Dust
Model | Abs. | Size
Backgr. | No | Small
Smoke | Yes | Small
Dust | Yes | Large
TOA
CM
AOT
0.47
0.412
0.66
2.13
- proxy of aerosol
reflectance

0.65
0.47
RA,TOA
background
smoke
dust
Reduction from BrC
0.41

## Slide 6
Aerosol Validation (2000-2016)
R
bias
rmse
Lyapustin, A., et al..: MAIAC MODIS Collection 6 Algorithm, AMT, in review

## Slide 7
km
MODIS
 MISR
(b)
km
HMISR-HMODIS
(a)
a) Histogram of MODIS-MISR plume height difference (2000-2008);
b) Standard deviation of retrieved plume heights.
RGB CM AOD0.47 Tb11 (K) Hs (km)
0 3.0
280 320
0 3.0
New: Aerosol Plume Height
Lyapustin, A.et al., Thermal Technique to Derive Smoke Plume Height from MODIS, Geophys. Res. Lett., to be submitted.
1. MAIAC is lower by about 200m in the histogram max, and by 448m on average.
2. 59.3% of MAIAC plume heights are found within 500m of MISR MINX values.

## Slide 8
Quality of Atmospheric Correction
CM Legend
Clear Land
Clear Water
Detected Smoke
Clouds
Cloud Shadows
296 - 2003

## Slide 9
Quality of Atmospheric Correction …
TOA RGB
BRF RGB
Decreasing brightness – moving from backscattering towards forward scattering
1200 km

## Slide 10
Interannual Variability
Amazon Browning and Greening Anomalies from MOD09 C5 (dashed) and MAIAC C6 L1B data (solid).
Anomaly Analysis – Myneni & Jian (BU)
Correlation with MEI – Hilker & Lyapustin
El Ninõ
La Ninã
Anomaly:
Significant interannual variability in MAIAC B/G anomalies and expected physical correlation with the short-term climate variations.
Hilker, T., A. I. Lyapustin, C. J. Tucker, F. G. Hall, R. B. Myneni, Y. Wang, J. Bi, Y. M. de Moura, P. J. Sellers (2014), Vegetation dynamics and rainfall sensitivity of the Amazon, PNAS, 111 (45), 16041-16046.

## Slide 11
Interannual Variability
Bi, J., R. Myneni, A. Lyapustin, Y. Wang, T. Park, C. Chen, K. Yan, Y. Knyazikhin, Amazon forests’ response to droughts: a perspective from the MAIAC product, Remote Sens., 2016.
Standardized anomalies for 2010 drought for MAIAC and MOD09 C5 and C6 NDVI, EVI
Amazon basin Greening and Browning area from MAIAC and MOD09 C5 and C6
NDVIn
EVIn

## Slide 12
Insect Forest Damage, Michigan Area
2009
2010
MAIAC MODIS 500m NDVI
Standardized Anomaly
RSAC Change Index
from 30m Landsat Data

## Slide 13
Chen, C., Y. Knyazikhin, T. Park, K. Yan, A. Lyapustin, Y. Wang, B. Yang and R. B. Myneni, Prototyping of LAI and FPAR Algorithm with MODIS MultiAngle Implementation of Atmospheric Correction (MAIAC) data, Rem. Sensing, 2017, 9, 370
MAIAC Red band BRF is higher than MOD09 9 – - so SSA in LUT was increased by up to 0.05;
No Red-NIR values outside of LUT boundaries;
Up to 10% more of high quality LAI/FPAR retrievals (main algorithm);
Improved LAI validation statistics:
- Slope: 0.890.97; Offset: 0.390.25;
- RMSE: 0.80.67; R2: 0.690.8
LAI/FPAR Alg. with MAIAC input
Validation over NA and SA:
DIRECT (sites) data from CalValPortal OLIVE (On Line Interactive Validation Exercise)

## Slide 14
MAIAC Snow Detection
Cooper, M. J., Martin, R. V., Lyapustin, A. I., and McLinden, C. A.: Assessing snow extent data sets over North America to inform and improve trace gas retrievals from solar backscatter, AMT, 11, 2983-2994, 2018.
Evaluated against Global Historical Climatology Network Daily (GHCN-D) database, over 80 000 surface stations worldwide (Menne et al., 2012a)
CMC: Canadian Meteorological Centre (CMC) Daily Snow
Depth Analysis Data (25km)
IMS: Interactive Multisensor Snow and Ice Mapping System (4km)
NISE: Near-real-time Ice and Snow Extent (SSM/I: 25km)

## Slide 15
MODIS De-Trending and X-Cal
New MCST RVS characterization for Aqua  new OBPG Terra Polarization Correction (PC) coefficients  MODAPS generated 50km L1B subsets for CEOS desert cal. sites;
Method: a) run MAIAC retrievals (AOT, BRDF etc.); 2) compute TOA reflectance (Rn) for fixed geometry (VZA=0, SZA=45) and evaluate trends in both Terra and Aqua; 3) Apply de-trending and compute T-A X-calibration factor (gain correction for T)
Lyapustin, A., Y. Wang, X. Xiong, G. Meister, S. Platnick, R. Levy et al, Science Impact of MODIS C5 Calibration Degradation and C6+ Improvements, AMT, 7, 7281-7319, 2014.
Chart: Terra TOA refl. (Rn), Egypt1, B1
 | ΔTerra | σTerra | ΔAqua | σAqua
TOA_B01 | -1.6884E-03 | 2.6114E-04 | 1.5848E-06 | 3.9377E-04
TOA_B02 | 7.7780E-04 | 2.4303E-04 | -6.5120E-05 | 3.5583E-04
TOA_B03 | -8.8922E-04 | 4.5314E-04 | -3.1763E-04 | 2.8486E-04
TOA_B04 | -5.6629E-04 | 3.2829E-04 | -3.9831E-05 | 5.0202E-04
TOA_B05 | 1.9477E-04 | 3.3019E-04 | 4.5784E-06 | 3.3528E-04
TOA_B06 | -3.9516E-04 | 3.0211E-04 | -3.1194E-04 | 2.8191E-04
TOA_B07 | 2.0259E-04 | 2.4491E-04 | -5.8419E-04 | 3.2705E-04
TOA_B08 | -1.2627E-03 | 1.0018E-03 | -5.5178E-04 | 1.0915E-04
TOA_B09 | -3.9874E-04 | 5.2176E-04 | 1.3724E-04 | 2.1120E-04
TOA_B10 | -7.2800E-04 | 8.2601E-04 | -3.0632E-04 | 7.1498E-04
Average trend/year/unit_refl.
Chart: De-trended Terra TOA refl. (Rn), Egypt1, B1

## Slide 16
Terra-Aqua X-Calibration
After MCST RVS de-trending for Aqua, we see trend reduction (a factor of 12 in B1 and a factor of 2 in B3) compared to our previous analysis.
 | Average | Stdev
TOA_B01 | 1.018776 | 0.000949
TOA_B02 | 1.000523 | 0.001054
TOA_B03 | 0.989436 | 0.001268
TOA_B04 | 1.00109 | 0.001448
TOA_B05 | 0.98862 | 0.001855
TOA_B06 | 0.997128 | 0.000898
TOA_B07 | 0.999368 | 0.000373
TOA_B08 | 1.003774 | 0.000948
TOA_B09 | 1.0014 | 0.001488
TOA_B10 | 1.014141 | 0.002077
Average X-gain for Terra
Chart: Aqua & Terra Rn after de-trending and x-calibration
Chart: Aqua & Terra Rn after de-trending (Egypt1, B1)

## Slide 17
DOY 60
2005
DOY 230
2005
AOD
CWV
BRF
SF
Ki: RGB RTLS
AOD
CWV
BRF
SF
Ki: RGB RTLS
https://landweb.modaps.eosdis.nasa.gov/cgi-bin/browse/browseMODIS.cgi
MAIAC Global Products

## Slide 18
Atmospheric File: MCDA2 (daily)

## Slide 19
Surface Reflectance File: MCDA1 (daily)

## Slide 20
BRDF/Albedo File: MCDA3 (8-day)

## Slide 21
MAIAC Products QA Bits
15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
AOD QA Bits
Cloud Mask
Land/ Water Mask
Adjacency Mask
AOD QA
Glint
AOD Model
Least Significant bit
Most Significant bit
15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
BRF QA Bits
Cloud Mask
Land/ Water Mask
Adjacency Mask
AOD
Level
Snow
BRF
Change Mask
Least Significant bit
Most Significant bit
Initialization status
High Altitude
Code Example:
Following c code pieces will retrieve Cloud Mask and Land Water Mask from QA:
unsigned short int qa;
unsigned char cm, lwmask;
cm = qa %8;
switch (cm):
{
case 0: //undefined
….
case 1: // clear
….
case 2: //Possibly cloud
}
lwmask = (qa/8)%4;
switch (lwmask)
{
case 0: //land
….
case 1: //water
….
}

## Slide 22
Geometric Normalization of MAIAC BRF
In order to normalize MAIAC BRF to any give angle, one need MAIAC BRF file and 8-day RTLS file.
Assume:
BRF is the retrieved surface reflectance (read from BRF file)
BRFn is the normalized reflectance (to be calculated)
Fv , Fg are the RTLS kernel function values at satellite overpass geometry (can be read from BRF file at 5km resolution)
F0v, F0g are the kernel function values at geometry to be normalized to (table 1 in users guide gives those values for any solar angle at nadir view)
Ki, kv, kg are the RTLS model parameters (read from closest 8-day RTLS file)
Then:
BRFn = BRF*(Ki + Kv*F0v+ Kg*F0g) / (Ki + Kv*Fv + Kg*Fg)