## Slide 1: Burned Area Mapping and Monitoring Algorithms
Louis Giglio
Department of Geographical Sciences
University of Maryland
9th International EOS/S-NPP Direct Readout Conference
21-24 June 2016

## Slide 2: Co-Is and Collaborators
Luigi Boschetti, University of Idaho
David Roy, South Dakota Sate University
Chris Justice, UMD
Wilfrid Schroeder, UMD
Joanne Hall, UMD
Krishna Vadrevu, UMD

## Slide 3: Focus
Focus will be on status of moderate/low resolution burned area mapping using MODIS and VIIRS.
NASA sponsored
  MCD45A1
  MCD64A1

## Slide 4: Landsat-8/Sentinel-2 Clarification
Landsat-8 (early 2013)
  OLI (15, 30 m)
  TIRS (100 m); failed Dec. 2014
Sentinel-2A (mid-2015)
  MSI (10, 20, 60 m)
Sentinel-2B (mid-2016?)
  MSI (10, 20, 60 m)
Likely topic for NDRC-10.

## Slide 5: Overview
Current C5.1 MODIS burned area products
  2008 IPOPP DR implementation
Forthcoming C6 MODIS burned area product
Forthcoming VIIRS burned area product
Vision for a true NRT DB implementation

## Slide 6: MODIS C5.1 Burned Area Products
MCD45A1 | 500-m Monthly L3
MCD45A1-based GIS Products (SCF) | Shapefiles + 500-m GeoTIFF
MCD64A1 (SCF) | 500-m Monthly L3
For all products burning is mapped to the nearest day.

## Slide 7: MODIS C6 Burned Area Products
MCD64A1 | 500-m Monthly L3
MCD64A1-based GIS Products (SCF) | Shapefiles + 500-m GeoTIFF
Should be released late this year.
Waiting primarily on validation.

## Slide 8: The challenge: change detection of Burned Areas
BRDF Effects
gaps
Day of burning
Persistence of the signal
D. Roy

## Slide 9: Algorithm/Product Characteristics
MCD45A1
Predictive BRDF model
500-m, daily
Uses no active fire data
Less noise-tolerant
Poorer mapping under cloudy conditions
Better mapping of cropland burning
MCD64A1
Supervised classifier
500-m, daily
Exploits active fire data
More noise-tolerant
Better mapping under cloudy conditions
Poorer mapping of cropland burning

## Slide 10
Wikimedia Commons
MCD45
MCD64
Notes: Photo credits: Wikimedia Commons

## Slide 11
Wikimedia Commons
MCD45
MCD64
Original plan for C6 was to merge features of the two different approaches to produce a better C6 product, i.e., a “Koala Goat”.
Notes: Photo credits: Wikimedia Commons

## Slide 12
Wikimedia Commons
MCD45
MCD64
Notes: Photo credits: Wikimedia Commons

## Slide 13
C5.1 MCD45
C5.1 MCD64
Large burn in Botswana, Aug.-Sep. 2008
~ 100 km

## Slide 14
Algorithm published in 2009. Product known by various names (“Direct Broadcast Burned Area Product”), but ultimately “MCD64”.

## Slide 15
burn
band 5 (1.2 m)
band 7 (2.1 m)
VI57

## Slide 16
burn
VI57
Both magnitude of drop and post-burn level depend on many variables -- fixed thresholds inappropriate.
band 5 (1.2 m)
band 7 (2.1 m)

## Slide 17: MCD64 Approach
Use “cleaned” active fire maps to select burned and unburned training samples from temporal composites
Extract conditional PDFs for burned and unburned pixels
Assign prior burned probability to each pixel
Bayesian classifier + supplementary relative threshold tests
Final contextual relabeling phase

## Slide 18
DAILY SURFACE REFLECTANCE
DAILY ACTIVE FIRE MASKS
TEMPORAL COMPOSITES
LAND COVER
VI*, VI*post
S*, t*, tf
IQR*pre, IQR*post
TRAINING MASK
TEMPORAL TEXTURE
SPATIAL PRIORS
INITIAL CLASSIFICATION
CONDITIONAL PDFs
CONTEXTUAL FILTER
BURN MAP
C6 MCD64
Algorithm
primary role of active fire map
change summaries
p(nb ≤ N|B)

## Slide 19
Maximum decrease in VI
Post-decrease VI
Day of maximum decrease
Active-fire date
Northern Australia, approx. August-October 2001
Change-summary examples:

## Slide 20
Region growing seeded with “cleaned” active fire map to identify burned and unburned training pixels…

## Slide 21
burned training pixel
unburned training pixel

## Slide 22
burned
unburned
Conditional PDFs

## Slide 23
burned
unburned
dynamic threshold
Conditional PDFs

## Slide 24
Final result: Date of burn for each 500-m grid cell

## Slide 25
MODIS C6 Burned Area Early Results
Overall increase in burned area relative to C5
  9% to 22% globally pending final tuning
  Modest loss of burned area in boreal tiles
    Huge number of new small lakes in C5.1 MCD12Q1
    Sporadic “dark” grid cells in surface reflectance input
Improved (i.e., smaller) temporal uncertainty
Final contextual relabeling phase now guided by neighbor statistics derived from training data
  True small burns much less likely to be discarded
Mapping of cropland burning somewhat cosmetically improved
  Timing can still be off due to confusion with harvest

## Slide 26
September 2006, MODIS tile h13v09 (eastern Brazil)
C5.1 MCD64A1
C6 MCD64A1

## Slide 27
Regional 2006 Burned Area Totals (× 104 km2 = Mha)
Region C5.1 C6
Global 341.8 374.6 9.6%
Boreal North America 1.9 1.8 -5.8%
Temperate North America 2.7 3.3 23.9%
Central America 1.5 2.2 47.2%
NH South America 2.2 4.2 89.7%
SH South America 11.5 20.5 78.7%
Europe 0.6 0.7 18.7%
Middle East 0.7 1.2 67.2%
NH Africa 114.5 113.8 -0.6%
SH Africa 121.9 129.0 5.8%
Boreal Asia 4.5 6.1 34.7%
Central Asia 18.0 23.4 30.0%
Southeast Asia 5.9 9.4 59.3%
Equatorial Asia 2.8 3.1 11.8%
Australia and NZ 53.2 55.7 4.8%
Preliminary!

## Slide 28: Collection 6 Validation
Landsat-8 imagery
CEOS burned area validation protocol
  Image-pair interpretation
    Cloud free + within a set time period (~2 months)
  Widely tested and used in peer reviewed literature
CEOS “Stage 3”
  “Product accuracy has been assessed, and the uncertainties in the product well established via independent measurements made in a systematic and statistically robust way that represents global conditions.”

## Slide 29: C6 Validation: Design Based Sampling
Stratified random sampling
  Statistically robust sampling essential for proper characterization of presence/absence of fire
    Current validation datasets are biased and are not suitable for detecting false positives
Stratification
  In space: sub-continental regions
  In time: fire seasonality based on MODIS active fire detections
Validate temporal and spatial aspects separately

## Slide 30
RED: ‘High Fire’ stratum
GRAY: ‘Low Fire’ stratum

## Slide 31
Temporal Uncertainty (Global, 2006)

## Slide 32: VIIRS Burned Area Product
Adapt MCD64 code to use VIIRS data
500-m monthly product
  Consistency with MODIS product
  Compromise between M- and I-band spatial resolution
  Burns mapped on daily basis
Same L3 10° × 10° MODIS sinusoidal tiles
HDF4 ➞ HDF5 format

## Slide 33: VIIRS Burned Area Product
Shapefiles and GeoTIFF files produced at SCF
0.25° CMG
Validate with same Landsat-8-based reference data used for MODIS Collection 6

## Slide 34: VIIRS Burned Area Product
Uses 750-m VIIRS bands M5, M7, M8, M11
VIIRS MCD64A1 (“VNP64A1”) prototyped with daily, 1-km VIIRS surface reflectance product as placeholder
March 2017 production code delivery to Land SIPS

## Slide 35
MCD64A1 Burn Date
Australia (h30v10), 1 March – 31 August 2014
MODIS
VIIRS

## Slide 36
VIIRS*
MODIS
VIIRS VNP64A1 Prototype
*1-km interim VIIRS daily surface reflectance product used as stand-in for 500-m VIIRS daily surface reflectance.

## Slide 37: C5 MCD64A1 DB Implementation
IPOPP burned area SPA released 2008
  C5 (vs. C5.1) code
Ingests daily corrected reflectance + daily Terra/Aqua MODIS fire-mask composites
All input data coregistered in MODIS sinusoidal projection
Temporal window and look-ahead limited to reduce nominal one-month production lag
Processes one “tile-month” in ~1 hour

## Slide 38: NRT Burned Area Mapping
Rapid production
  Cumulative map through day N available on day N
  Map is refined as additional days are acquired
Sacrifice mapping of smallest burns for NRT
Leverage active fire data more heavily
  MCD64 prior probabilities

## Slide 39: NRT Burned Area Mapping
Straightforward integration with MAIAC
  Leverage consistent observation geometry, improved cloud masking, reduced noise, etc.
Focus on VIIRS
Seeking funding