## Slide 1: SeaDAS 7 for Ocean Data Users
Fred Patt
Sean Bailey
and the OBPG SeaDAS Team
June 23, 2016

## Slide 2
Enabling the Study of our Planet from Space
“Standardizing Satellite Data”
Free and publicly available software developed by NASA which enables users from their standard desktop and laptop computers to process, visualize, and analyze remote-sensing data.

## Slide 3: SeaDAS Overview
SeaDAS is a comprehensive open-source toolbox and development platform for viewing, analyzing and processing of remote sensing data.
  nearly 20 years as a tool for the ocean color community
  it has two primary components, visualization and science data processing that can exist independently
  original GUI package development used IDL
  evolved from “PC-SEAPAK” developed for CZCS data in the late 1980s
GUI redesign began in 2009 based on the BEAM, with extensions that provide the functionality provided by previous versions of SeaDAS
  first official release of SeaDAS version 7 was April 2013
OCSSW
Ocean Color Science SoftWare package
SeaDAS
BEAM
core
OCSSW
Tool
Integration
User Interface
Look & Feel
Tool Modification
Modules

## Slide 4: Description & Significance
Vision and Strategic Goals
  NASA:
    “Advance understanding of Earth and develop technologies to improve the quality of life on our home planet.” (2014)
  SeaDAS
    Provide the user community with the tools to work with supported satellite mission data
    Identically reproduce all standard products, including levels 1, 2 and 3
    Continually evolve to keep up with technology
Accessibility
  Software (open-source)
    Runs on standard inexpensive desktop and laptop computers
  Data (freely available)
User Community
  Research Scientists
  Anyone
Standardizes Satellite Data
  Supports over 16 remote-sensing satellite missions

## Slide 5: Description & Significance
Supported Satellite Missions
  Aquarius
  AVHRR
  CZCS
  GOCI
  HICO
  LANDSAT-8 OLI
  MERIS
  MODIS Aqua
  MODIS Terra
  MOS
  OCM1
  OCM2
  OCTS
  OSMI
  SeaWiFS
  VIIRSN
  ... coming soon Sentinel-3 (OLCI)

## Slide 6: Components
Visualization and Analysis
  mapping and reprojection*
  cropping and subsetting
  bathymetry and topography
  masking and overlays
  band combinations (rgb imagery)
  mosaic and file merging
  band smoothing
  custom algorithms (band math)
  statistics
  scatterplots
  color palettes
Satellite Data Processing
  processors installer
  processors (l2gen, l3bin, l3mapgen, …)
  multilevel processor
SeaBASS field measurement integration

## Slide 7: Supported Data Formats
SeaDAS supports a growing number of raster data formats:
GeoTIFF
NetCDF
HDF (HDF4, HDF5, HDF-EOS)
ENVI (BIL/BIP)
Additional targeted support for specific data formats of other EO sensors such as MODIS, AVHRR, AVNIR, PRISM and CHRIS/Proba.
BEAM-DIMAP (Digital Image Format)
  Originally developed to support the SPOT mission
  Data are stored as a single product header file with the suffix .dim in XML format containing the product meta-data

## Slide 8: Layout & Toolbars

## Slide 9: File Manager
Displays loaded files in a tree view
  Metadata
  Flag codings
  Vector data
  Bands (products)
Enables selection of a band
Convenient right-click options
  Band properties and renaming
  Vector export

## Slide 10: File Manager

## Slide 11: Image View
Screen interactive modes
  Pan & zoom (default)
  Selection
  Rectangle zooming tool
Auto-zoom options
  Match screen resolution
  Fill window
Multiple image views
  Window tiling
  Synchronized boundaries/zoom
  Show synchronized cursor
  Windows are not floatable
Stores/contains layers
Stores/contains mask visibility
Image rotation
Image export

## Slide 12: Image View

## Slide 13: Mask View
Masks
  l2flags
  Geometries
  Logical math expression
  Coastline
  Land
  Bathymetry
Region of Interest (ROI) Mask
Mask Manager Tool
  add/modify/delete
  show/hide
  color, transparency
Stored in file
  shared by all bands
Chlorophyll level-2 image, masks displayed:
COASTZ (black), CLDICE (white), LAND (brown)

## Slide 14: Mask Manager

## Slide 15: Layers
Layers
  band image
  color bar
  contours
  GCP
  geometries
  masks
  map gridlines
  no-data
  pins
  world map
Layer Manager Tool
  add/remove
  show/hide
  stack order
  transparency
  edit (Layer Editor Tool)
Stored independently in each image view
Can only be saved in a session
Chlorophyll on US Eastern continental shelf, layers displayed:
land mask (black), no-data (grey), map gridlines, color bar,
2000m isobath contour, coastline contour

## Slide 16: Layer Manager

## Slide 17: Color Manager

## Slide 18: Tools

## Slide 19: Map Gridlines

## Slide 20: Bathymetry & Elevation Tool

## Slide 21: Bathymetry & Elevation Tool

## Slide 22: Coastline, Land & Water Mask Tool

## Slide 23: Contour Lines Tool
50m
200m
1000m

## Slide 24: RGB Images

## Slide 25: RGB Images

## Slide 26: Analysis & Statistics
Statistics
Analysis Plots
  Correlative Plot
  Histogram Plot
  Profile Plot
  Scatter Plot
  Spectrum Plot
Uses ROI (Region-Of-Interest) Masking
Analysis restrictions
  All bands must be in same file (Collocate)
File Processing Analysis Tools
  Cluster (EM and K-Means)
  Principal Component
  Spectral Unmixing

## Slide 27: Shiptrack & SeaBASS

## Slide 28: Shiptrack & SeaBASS

## Slide 29: OCSSW Processors GUI
All Ocean Color Science Software processors have dedicated user interfaces in SeaDAS

## Slide 30: OCSSW Processing

## Slide 31: OCSSW Processing: l2gen

## Slide 32: OCSSW Processing: l2gen

## Slide 33: OCSSW Processors – l2bin
Generate a L3 bin file from one or more L2 files
Command line usage
l2bin parfile=parfile or
infile=infile ofile=ofile [sday=sday] [eday=eday]
resolve=resolve [flaguse=flaguse] [l3bprod=l3bprod]
[prodtype=prodtype] [noext=noext] [verbose=verbose
[rowgroup=rowgroup] [night=night]
parfile = parameter filename
infile = input filename/filelist
ofile = output bin filename
sday = start datadate (YYYYDDD) [ignored for "regional”]
eday = end datadate (YYYYDDD) [ignored for "regional”]
resolve = bin
flaguse = flags masked [see /SENSOR/l2bin_defaults.par]
l3bprod = bin products [default=all products]
prodtype = product type (Set to "regional" to bin all scans.) pversion = production version [default=Unspecified]
noext = set to 1 to suppress generation of external files
[default=0, (1 for "regional" prodtype)]
rowgroup = # of bin rows to process at once.
night = set to 1 for SST night processing [default=0]
qual_prod = quality product field name
qual_max = maximum acceptable quality [default=2]
verbose = Allow more verbose screen messages [default=0]

## Slide 34: OCSSW Processing: l3mapgen

## Slide 35: Multilevel Processor (MLP)
Allows for sequential end-to-end processing via a single script
Accessible via command line and the SeaDAS GUI
Programs that can be accessed:
  modis_L1A.py
  modis_GEO.py
  modis_L1B.py
  l1aextract_modis.py
  l1aextract_seawifs.py
  l1mapgen
  l1brsgen
  l2gen
  l2brsgen
  l2mapgen
  l2extract
  l2bin
  l3bin
  l3mapgen

## Slide 36: OCSSW Processing: Multi-level Processor

## Slide 37: How To Download
http://seadas.gsfc.nasa.gov/

## Slide 38: Help

## Slide 39: Help
SeaDAS Internal Help
  Located in Help menu
Ocean Color Web Page
  http://oceancolor.gsfc.nasa.gov
  SeaDAS
    http://seadas.gsfc.nasa.gov
    Web Version of SeaDAS Internal Help
    Tutorials
    Latest downloads
  Forum
  http://oceancolor.gsfc.nasa.gov/forum/oceancolor/forum_show.pl
YouTube Channel
  http://www.youtube.com/user/nasaoceancolor

## Slide 40
Questions?

## Slide 41
Backup

## Slide 42: Remote-Sensing Satellite Data Levels
Level 0 data
  unprocessed instrument/payload data
Level 1A data
  time-referenced and annotated with ancillary information including radiometric and geometric calibration coefficients and georeferencing parameters
Level 1B data
  instrument/radiometric calibrations applied
Level 2 data
  derived geophysical variables
Level 3 data
  derived geophysical variables that have been aggregated/projected onto a well-defined spatial grid over a well-defined time period
  Binned
    Each Level 3 binned data product consists of the accumulated data for all L2 products in a product suite, for the specified instrument and resolution, corresponding to a period of time (e.g. daily, 8 days, monthly, etc.) and stored in a global, nearly equal-area, integerized sinusoidal grid (ISIN)
  Mapped
    Created from the corresponding Level 3 binned products – Each Standard Mapped Image (SMI) file contains a Plate Carrée, pixel-registered grid of floating-point values (or scaled integer representations of the values) for a single geophysical parameter